## Slide 1
Aktorik und Sensorik mit intelligenten Materialsystemen 4
Computer Lecture: Nonlinear control of a SMA-spring actuator
Gianluca Rizzello
gianluca.rizzello@mmsl.uni-saarland.de Saarland University

## Slide 2: Computer Lecture Overview
GOALS:
  PI position control for a SMA-spring actuator
  Implementation of sliding mode position control
  Comparison among the two controllers

## Slide 3: Assignment
Given the Simulink file representing the SMA-spring model:
Design and implement a PI controller for the SMA actuator, based on the following linearized model, in such a way that the closed loop system is a first order transfer function with time constant t* = 0.02 s.
Considering J bounded between 0 and 0.25 W, implement a sliding mode control architecture. Implement an arbitrary chattering-avoiding configuration, with e chosen arbitrarily.
Compare the performance of both controllers in tracking a sinusoidal reference as where A and f are free parameters. Consider different values of f (e.g., 1 Hz, 3 Hz, 5 Hz) and A (e.g., 0.0005, 0.001, 0.0015), and see how the two controllers perform in both cases. NOTE: in case simulation time is too large, you can deactivate the computation of internal hysteresis loops via the variable params_PC2.internal_loops_flag in Parameter_PC2.m file