## Slide 1
Aktorik und Sensorik mit intelligenten Materialsystemen 4
ASIM 4 Final Exam Assignment: SMA Actuated Wing
Gianluca Rizzello
gianluca.rizzello@mmsl.uni-saarland.de Saarland University

## Slide 2: ASIM 4 Final Exam: SMA Wing
System layout: two rigid rods of lengths l1 and l2 are connected through two rotational joints of radii r1 and r2, and actuate by bundles of SMA wire actuators
By controlling the Joule heating of the SMA wires, rotation angles of both joints q1 and q2 can be controlled
SMA 1A
SMA 1B
q1
q2
SMA 2A
SMA 2B
2r2
2r1
l2
l1

## Slide 3: ASIM 4 Final Exam: SMA Wing
Project guidelines:
  Study the effects of control inputs JSMA,1A , JSMA,1B, JSMA,2A, and JSMA,2B on the actuator performance, in terms of q1 and q2, with all Joule heating signals limited between 0 and 2 W;
  Define control inputs u1 and u2, such that if u1 ≥ 0 then JSMA,1A = |u1|, JSMA,1B = 0 if u1 < 0 then JSMA,1A = 0, JSMA,1B = |u1| if u2 ≥ 0 then JSMA,2A = |u2|, JSMA,2B = 0 if u2 < 0 then JSMA,2A = 0, JSMA,2B = |u2|
  Find a linear approximation of the responses between u2 and q2 (for u1 = 0),
  Design and compare linear controllers for position regulation of q2
  Design and compare linear controllers for trajectry tracking of q2
  Compare linear and nonlinear controllers for q2
  Repeat the above identification/control steps for the u1 – q1 response (with u2 = 0)
  Test the performance of both controllers when they work together to control q1 and q2 at the same time
  Compare continuous-time and discrete time controllers obtained with different sampling times and discretization methods, as well as the effects of anti-windup
  Test the control system response when disturbanced td are affecting the actuators
  Test the control system response when environmental temperature TE is changing
  Compare sensor-based and sensorless control based on resistance signals

## Slide 4: ASIM 4 Final Exam: SMA Wing
Structure model
SMA
lSMA
FSMA
t
JSMA
td
q
t = -JT(q)FSMA
lSMA(q)
Euler -Lagrange

## Slide 5: ASIM 4 Final Exam: SMA Wing
SMA bundle model
SMA
JSMA,K
lDE,K
FSMA,K
K = {1A, 2B, 2A, 2B}

## Slide 6: ASIM 4 Final Exam: SMA Wing
Kinematic model
Jacobian matrix

## Slide 7: ASIM 4 Final Exam: SMA Wing
Kinetic energy
Potential energy
Lagrangian

## Slide 8: ASIM 4 Final Exam: SMA Wing
Euler-Lagrange model
Definition of above quantities

## Slide 9: ASIM 4 Final Exam: SMA Wing
Complete model in compact form
Inverse of inertia matrix