## Slide 1
Aktorik und Sensorik mit intelligenten Materialsystemen 4
Computer Lecture: PID Position Control of a DE-Mass Actuator
Gianluca Rizzello
gianluca.rizzello@mmsl.uni-saarland.de Saarland University

## Slide 2: Computer Lecture Overview
GOALS:
  PID position control design for a DE-mass actuator
  Model-free PID tuning via Ziegler-Nichols method
  Model-based PID design
  Introduction of harmonic compensator for sinusoidal tracking

## Slide 3: Assignment
Given the Simulink file representing the DE-mass model:
Design a PID control based on Ziegler-Nichols method. For generating the step, use Reference 1. Simulate the closed loop behavior of the DE in response to References 2 and 3.
Consider the following linear model, representing an approximation of the DE around equilibrium position corresponding to v = 1000 V Based on this model design a filtered PID controller, by imposing in closed loop a second order behavior with d = 0.75, t* = 0.05 s. Simulate the closed loop response of both G(s) and the DE to References 2 and 3.
Repeat design of point 2) by choosing instead d = 0.75, t* = 0.01 s. Simulate both G(s) and the DE in closed loop, and compare results with 2).
Test the performance of the filt. PID in tracking Reference 4, i.e., a 1 Hz sine.
Implement, in parallel with the previous filt. PID, an Harmonic compensator for tracking sinusoidal signals at 1 Hz (2p rad/s). Tune the gain of this harmonic compensator by hand. Test the performance of the PID + harmonic compensator in tracking References 4 and 5.
NOTE: the input voltage of the DE must always range 0 V and 2500 V.