## Slide 1
Aktorik und Sensorik mit intelligenten Materialsystemen 4
Computer Lecture: Digital control of a SMA-spring actuator
Gianluca Rizzello
gianluca.rizzello@mmsl.uni-saarland.de Saarland University

## Slide 2: Computer Lecture Overview
GOALS:
  Digital PI position control for a SMA-spring actuator
  Simulation for different sampling times
  Simulation for different discretization methods
  Implementation of anti-windup architecture

## Slide 3: Assignment
Given the Simulink file representing the SMA-spring model:
Design and implement a PI controller for the SMA actuator, based on the following linearized model, in such a way that the closed loop system is a first order transfer function with time constant t* = 0.015 s.
Implement the controller as a digital PI, by choosing a preferred discretization method for the integral. Choose the sampling time as where t is the time constant of the SMA model transfer function G(s). Simulate the closed loop performance for N = 20, 10, 5, 2, for a test of the duration of 1 second in which a step reference starts at 0.104 m and switches to 0.103 m at t = 0.5 s.
For the case with N = 2, simulate the closed loop performance obtained by using the other two discretization methods
Choose N = 10 and a preferred discretization method. Simulate the closed loop performance for a test of the duration of 1 second in which a step reference starts at 0.104 m and switches to 0.102 m at t = 0.5 s. Implement an arbitrary anti-windup architecture. Compare the performance obtained with and without the anti-windup scheme, considering J limited within 0 W and 0.25 W.